## Slide 1: Cosc 2030
Code Optimization and Performance

## Slide 2: Optimization and Performance
The performance and optimization is a critical aspect of any programming, as it can significantly impact the speed and efficiency of your applications.
we'll explore various techniques and best practices for optimizing your code.
Some are obvious, other are less so.
  Most of these will not change the over all algorithm, but minor changes can cause either great speed ups or slow downs.

## Slide 3: Use the right data structures.
This is likely the most obvious and the point of this course.
  Why use a Dequeue vs a Vector?
  These are the questions we have been exploring all semester.

## Slide 4: Memory
Avoid any unnecessary copying of variables.
  The system need to allocation and later deallocation the memory. In a loop this can make things very slow.
  slow version
    char c = word[i]; //actually there is some debate here about cache and registers.
    if (c == ‘a’)
  faster version (also just less code too)
    if (word[i] ==‘a’)
Also avoid declaring variables inside of loops for the same reason
  slow version: for(i=0; …) { char c; …. }
  faster version: char c; for(i=0;…) { … }

## Slide 5: Memory (2)
Avoid whenever possible copying methods “call by value”.
  each time you call a function a with a “call by value”, it needs to make a copy of the data before sending to the method/function/subroutine.
When ever possible use the stack and not the heap memory.
  Allocate objects on the stack whenever possible, as stack allocation is faster than heap allocation. Use dynamic allocation (e.g., new and delete) only when the object's lifetime extends beyond the current scope.
  example:
    int value =42; //stack allocation
    int * value = new int; *value = 42; //heap allocation.

## Slide 6: Memory (3)
Excessive memory allocation and deallocation can lead to performance issues.
  new/delete
  as before declaring variables inside loops.
  Allows being things, Do I really need that variable? Can I reuse it? Should be declared might higher up in the code.
  interesting c++ issue.
    x++ and ++x result in the same value.
    x++ requires the use of a temporary variable included by the compiler while ++x does not. So use ++x instead of x++.

## Slide 7: Cache and memory awareness.
Program structure. Is the language row or column ordered for arrays?
  Int[128,128] data;
  Each row is stored in one page
  Program 1
  for (j = 0; j <128; j++) for (i = 0; i < 128; i++) data[i,j] = 0;
    128 x 128 = 16,384 possible cache and memory page faults
  Program 2
  for (i = 0; i < 128; i++) for (j = 0; j < 128; j++) data[i,j] = 0;
    128 possible cache and memory page faults

## Slide 8: Cache and memory awareness (2)
From Wiikipedia:
Row-major order
  C/C++/Objective-C (for C-style arrays), PL/I, Pascal, Speakeasy, and SAS.
Column-major order
  Fortran, MATLAB, GNU Octave, Julia, S, S-PLUS, R, Scilab, Yorick, and Rasdaman.[12]
Java and python is neither, as they does not store arrays contiguously.
  Java stores a table of pointers for 2D arrays.

## Slide 9: Optimize your Loops.
Loops are often the core of algorithms.
Optimize loops by minimizing loop overhead, reducing unnecessary calculations, and using the right loop constructs
Example:
for(int i=0; I <100; i++) for(int i=1; i<100; i+=2)
if (i%2 ==1)
cout <<i<<“ is odd” cout <<i<<“ is odd”

## Slide 10: Optimize your Loops (2)
Loop fusion combines loops that use the same data elements, possibly improving cache performance and faster execution.
For example:
becomes
  for (i = 0; i < N; i++)
  C[i] = A[i] + B[i];
  for (i = 0; i < N; i++)
  D[i] = E[i] + C[i];
  for (i = 0; i < N; i++)
  { C[i] = A[i] + B[i];
  D[i] = E[i] + C[i]; }

## Slide 11: Optimize your Loops (3)
Loop fission splits large loops into smaller ones to reduce data dependencies and resource conflicts.
A loop fission technique known as loop peeling removes the beginning and ending loop statements.
For example, becomes
  A[1] = 0;
  for (i = 2; i < N; i++)
  A[i] = A[i] + 8;
  A[N] = N;
  for (i = 1; i < N+1; i++)
  { if (i==1)
  A[i] = 0;
  else if (i == N)
  A[i] = N;
  else A[i] = A[i] + 8; }

## Slide 12: Loops and working with the hardware.
Loop unrolling is the process of expanding a loop so that each new iteration contains several of the original operations, thus performing more computations per loop iteration. Allows for more parallel instructions are the assembly level.
For example:
becomes
  for (i = 1; i <= 30; i++)
  a[i] = a[i] + b[i] * c;
  for (i = 1; i <= 30; i+=3)
  { a[i] = a[i] + b[i] * c;
  a[i+1] = a[i+1] + b[i+1] * c;
  a[i+2] = a[i+2] + b[i+2] * c; }

## Slide 13: Reduce Functions calls
Slow version
Int square(int x) {
return x* x;
}
int main() {
for( int i=0; i< 100; i++)
cout <<square(i);
}
faster version
int main() {
for( int i=0; i< 100; i++)
cout <<i*i;
}
You can also use the compile optimization command inline to have the compiler inline functions.
But it’s almost always better/faster if you do it yourself. reducing variables.

## Slide 14: Reduce Functions calls
Each time a function/method/subroutine is called,
  create a spot on the stack
  copy any parameters into the stack frame
  call the function
  place the return pointer
  create local variables.
  run the code of the function
  place return value, if necessary, in stack
  use the return pointer to go back to calling code segment.

## Slide 15: Functions, return values, and temp variables.
whenever possible use the return statement instead of creating temp variables and returning temp.
  bool ret = size ==0;
  return ret;
VS
  return size==0;
While trivial, you remove a variable, memory, and a copy. A test of 100 millions calls shows a difference of 4 seconds compares to 1 second.

## Slide 16: Case vs if statement.
When you are comparing numbers in a set of if, else if use a case
For example, instead of the following code:
if (a[i] == 1) f();
else if (a[i] == 2) g();
else if (a[i] == 5) h();
write the following code:
switch (a[i]) {
case 1: f(); break;
case 2: g(); break;
case 5: h(); break;
}
The compiler can take advantage many optimizations to make a switch statement faster.

## Slide 17: Conclusion
Optimization efforts pay the biggest dividends when they are applied to code segments that are executed the most frequently.
  In short, try to make the common cases fast.

## Slide 18: Some timing and efficiently questions
finish in Time: 0.05
tim.Start();
ofstream out("file1.txt");
for(int i =0; i<size; i++)
out<<"Misspelled"<<endl;
out.close();
tim.Stop();
printf("finish in Time: %.2f\n",tim.Time());
finish in Time: 14.46
tim.Start();
//print out results
for(int i =0; i<size; i++) {
of.open("file2.txt", ios::app);
of<<"Misspelled"<<endl;
of.close();
}
tim.Stop();
printf("finish in Time: %.2f\n",tim.Time());
int size =30000;

## Slide 19: Clean word runs.
Cleanword,
  no return value, call by reference. All changes made to the parameter string, no local variables.
    Pi times, 1.23 seconds
  String return value, string parameter call by value, local return value. No changes made to the parameter.
    Pi times, 1.44 seconds
  String return value, string parameter call by value , no changes made to parameter, but char c = word[i] at the top of the loop.
    Pi times, 1.39
  String return value, string parameter call by reference, , no changes made to parameter, char c = word[i] at the top of the loop.
    Pi times, 1.28
  String return value, const string parameter call by reference, , no changes made to parameter, but char c = word[i] at the top of the loop.
    Pi times, 1.30 (surprised, this should have been a little faster).

## Slide 20: Profile your code
Use a profiler to identify performance bottlenecks in your code. This will help you focus your optimization efforts on the parts of your code that will have the biggest impact.
How to for python https://realpython.com/python-profiling/
Open source profiles for Java https://java-source.net/open-source/profilers

## Slide 21: Popular ones for c++
Valgrind
  Valgrind is a powerful profiling tool that can detect memory leaks, thread errors, and other performance issues. It provides a suite of tools, including Memcheck, which can help you identify memory errors in your C++ code.
Google Performance Tools (gperftools):
  gperftools is a collection of profiling and performance analysis tools for C++ code. It includes a CPU profiler, a heap profiler, and a heap-checker tool that can help you identify memory leaks and other memory errors.
Intel VTune:
  Intel VTune is a performance analysis tool that can help you analyze and optimize the performance of C++ code running on Intel processors. It provides a wide range of profiling features, including CPU profiling, memory profiling, and thread profiling.
Linux perf:
  Linux perf is a performance analysis tool that is included in the Linux kernel. It provides a suite of profiling tools, including CPU profiling, memory profiling, and kernel tracing, that can help you identify performance bottlenecks in your C++ code.

## Slide 22: Gprof example
g++ -g callfuntest.cpp –o callfun -pg
gprof callfun > output
% cumulative self self total
time seconds seconds calls ns/call ns/call name
40.09 0.04 0.04 981990 40.83 40.83 cleanword5
20.05 0.06 0.02 981990 20.41 20.41 cleanword2
20.05 0.08 0.02 981990 20.41 20.41 cleanword3
10.02 0.09 0.01 981990 10.21 10.21 cleanword

## Slide 23: Gprof example (2)
% time the percentage of the total running time of the program used by this function.
cumulative seconds a running sum of the number of seconds accounted for by this function and those listed above it.
self seconds the number of seconds accounted for by this function alone. This is the major sort for this listing.
calls the number of times this function was invoked, if this function is profiled, else blank.
self ms/call the average number of milliseconds spent in this function per call, if this function is profiled, else blank.
total ms/call the average number of milliseconds spent in this function and its descendents per call, if this function is profiled, else blank.
name the name of the function.

## Slide 24
Q
A
&